TA-25Mini CI Mini stereo amplifier with Limiter
The TA-25Mini is an efficient, cost-effective choice for home and commercial installations in restaurants, pubs, shops, conferencing rooms, fitness clubs for background music playback. It is ideal for simple installations or as a part of big installations.

The TA-25 Mini utilizes advanced materials, state of the art engineering and innovate design by an international team of professional designers.
It delivers pure and distortion-limited power as well as rich sound performance with stunning accuracy, soundstage and sensational dynamics.
Features
- Easy placement thanks to small dimensions and weight;
- Low working temperature (Class D amp) and external power supply allows for placement in closed areas (for example in ceilings or walls);
- A single stereo input with 2 connection options (Unbalanced 3.5mm jack and balanced-pin screw terminal connectors);
- Limiter to prevent clipping of the power amplifier.
Specification
- Power Output: 2 x 25W  8ohm, Class D
- THD: Less or equal 0.08%
- Signal/Noise ratio: =>90dB
- Frequency Response: 30Hz – 18kHz
- Inputs: Stereo input
  - Unbalanced 3.5 mm AUX (47KΩ/1V)
  - Balanced – pin screw terminal connectors;
- Microphone Input: Sensitivity 7mV ; THD 1% ; Frequency resp. 200Hz – 15kHz (+/-3dB)
- AC Power, Power Consumption: DC 24V, max. 60W
- Dimensions (H x W x D): 3.2 x 15.8 x 11 cm
- Weight (net): 0.42 kg / pc.