BLAK INTEGRATED AMPLIFIER USB
The blak Integrated Amplifier USB has 150 watts of refined power for a smooth yet authoritative performance.  The blak Integrated also has a host of additional features such as an audiophile quality internal DAC with USB connection for computers and mobile devices, a high quality Moving Magnet phono input and aptX bluetooth wireless connectivity.

Features
- 3 x RCA line inputs
- 1 x Pair analogue XLR inputs
- MM phono input
- aptX Bluetooth input
- Circuit-switchable headphone output
- High quality internal DAC circuit (USB Amplifier only)
- Rear-located USB type-B port (USB Amplifier only)
- High audiophile grade components used throughout
- Top quality transformer design for optimum power
- Striking design and superlative build quality
- Brightness-adjustable oversize LED display
Specification

Inputs:	3 x RCA line inputs 1 x Pair analogue XLR inputs 1 x USB type-B input 24/192 & DSD compatible (only operational with ‘USB’ Version) MM phono input aptX Bluetooth input MM input – gain, 76.75dB@1kHz, input impedance 47k ohm, 150pF Line & XLR inputs – input impedance 24k ohm XLR, 40k ohm RCA
Gain:	@ 1kHz, 8ohm 36,75dB
THD:	@ 1W, 8ohm, 5kHz < 0.02% @ 12W, 8ohm, 5kHz < 0.035%
Power output:	@ 1kHz, 8ohm > 150W @ 1kHz, 4ohm > 230W
Frequency response:	@ -3dB, 12W, 8ohm from < 20Hz to more than 80kHz
Channel balance:	@ 1kHz, 8ohm, 12W better than 0.3dB
Cross talk:	@ 1kHz, 8ohm < -104dB
S/N:	@ 1kHz, 8ohm, 1W > 76dB
Dimensions:	(H x W x D) 140 x 440 (inc. faceplate) x 309mm / 140 x 400 (chassis) x 309mm
Weight:	14kg
Rated Power Consumption:	480W
Maximum Power Consumption:	800W