Animation Laser with ILDA 20K   + SD Card System
CR-TEC Surpass-1 high-performance brand ILDA 300mw green laser.

Features

- 2G SD storage system for ild standard ILDA files, simple to upload your favourite laser show
- Constant Temperature system diode with cooling and heating, being reliable, bright and sharp.
- The best laser safety: key switch, interlock, block-out without sound, dash free, eye-loop.
- High end Digital LCD Display Control System in rear panel
- 300mw green laser diodes, air-cooled
- ILDA control
- Easy to setup, equipped with LCD display
- X / Y flip the switch by analog volume
- Exposure control range
- KEY for external contacts, and emergency stop switch
Specifications
- Model: SURPASS-1 SD(G)
- Laser Power: 300mW Green
- Modes: ILDA, SD/Sound, Auto, DMX512, Master/Slave, ILDA, SD
- Power: AC100-240V Auto Switch
- Rating Power: 55W
- Mess: 385*280*196mm
- Weight: 8Kg