iSolution technology allows synchronisation of different types of intelligent iSolution fixtures via either a custom-built iLead DMX-512 controller or in stand-alone mode. iLead (Integrated Lighting System) allows fixtures to be linked and work in synchronisation, regardless of type, including iLead-equipped scanners, moving heads, and colour changers.

iSolution technology allows synchronisation of different types of intelligent iSolution fixtures via either a custom-built iLead DMX-512 controller or in stand-alone mode. iLead (Integrated Lighting System) allows fixtures to be linked and work in synchronisation, regardless of type, including iLead-equipped scanners, moving heads, and colour changers. The iLead controller can also remotely set the DMX addresses of the fixtures. All units are also controllable via any universal DMX-512 controller. Conversely, the iLead controller is a universal DMX-512 controller and can be used with non-iSolution fixtures.
Features
DMX-512 control channels: 16/8 Channels Switchable
Setting and addressing: 4 digit blue LED display
LED display with on/off setting function
Data in/out: Locking 3-pin XLR iSolution operation
Consistant DMX configeration enables iShow to be linked with iRock and iMove
DMX address can be set remotely by iLead controller.
No need to calculate the DMX channels of each fixture in the chain
When the DMX signal is off, the lights will switch to master/slave mode automatically
Easy installation, easy addressing, and easy operation Pre-programmed function
Automatic switching between music trigger or auto trigger mode
Master/Slave mode:
i.) No need to designate which unit is master or slave
ii.) Built in dynamic lighting shows for instant operation
User friendly easy controller:
Enjoy various lighting shows at your fingertips.
Pan/Tilt -Pan: 540 degrees; Tilt 270 degrees - Pan/Tilt resolution: 16-bit (16 channel) -
Automatic Pan/Tilt correction
Magnetic Pan/Tilt home positioning for easy calibration and maintenance
Gobo wheel - Static gobo wheel: 9 gobo's plus open (all replaceable)
Rotating gobo wheel: 7 rotating, interchangeable gobo's plus open
Magnetic gobo wheel home positioning for easy calibration and maintenance
Colour wheel - 9 trapezoid dichroic colours plus white - Rainbow effect in both directions
Magnetic colour wheel home positioning for easy calibration and maintenance
Effect wheel - Prism - Rotating prism
Dimmer/Shutter - 0-100% - independent shutter / variable speed strobe, 1 ~ 10 flashes per second Optics
Motorised iris for different beam diameters
Gobo Index- Auto Adjust image angle to display
High quality optical lens, dichroic colours and gobos
Beam Angle: 14 degrees
Specification
Power supply: 230v
Lamp: HMI 575w / MSI 575w
Replacement lamp: Lamp71 / 71a
Dimensions: 427 x 478 x 369mm
Weight: 27kgs