3W LED moving head lighting XLED 390 is low noise, low maintenance and energy saving. This bright and colourful unit extends another choice for users

3W LED moving head lighting XLED 390 is low noise, low maintenance and energy saving. This bright and colourful unit extends another choice for users.
Technical Data
Voltages: 100/120/200/220/230/240V AC, 50/60Hz
Power Consumption:
               260W@220V
Light Source:
              3W LEDS
              90 LEDS (30 Red+ 30 Green + 30 Blue)
Average service life:
              50,000 hours
Colors:   RGB Color mixing
Color Temperature:
               0~100% linearly adjustable
Dimmer:  0~100% linearly adjustable (8- or 16-bit)
Strobe:    0~25 F.P.S.
Beam angle:
                 Standard: 13°
                 Optional:  23°
Field angle:
                  Standard: 26°
                  Optional: 46°
Control and Programming:
               DMX 512, 5 pin interface
               Stand alone mode, Master/Slave operation and Self-testing mode
               RDM
DMX Channels:
               Short mode: 8, Standard mode: 13, Extended mode: 17
Head Movement:
               Pan 540°, Tilt:270°, (8- or 16-bit)
               Automatic Pan/Tilt position correction
               Adjustable Pan/Tilt speed
Display:   LCD, brightness and contrast adjustable
               DMX channel display
               Menu inversion display function
               Fixture and Lamp usage time display
Other features:
               Automatic fan speed control
               Automatically turn off power when LED temperature is too high
Ambient temperature:
               -20°C~40°C
Housing:  Composite plastic and aluminum (IP20)
Net weight: 11kg