Ypoc Basic 250 features high quality and modern technology. The high brightness in its class is achieved by combining a 250W discharge lamp with a high quality coated optical system.
Except the reduced set of features, it offers similar functions compared to the Ypoc 250. With 11 dichroic colors plus white, 9 static Gobos plus open, Shutter, Dimmer and a 4,5mW Laserdiode it offers the standard equipment for a washlight in his class.

Ypoc Basic 250 features high quality and modern technology. The high brightness in its class is achieved by combining a 250W discharge lamp with a high quality coated optical system.
Except the reduced set of features, it offers similar functions compared to the Ypoc 250. With 11 dichroic colors plus white, 9 static Gobos plus open, Shutter, Dimmer and a 4,5mW Laserdiode it offers the standard equipment for a washlight in his class.
Source
Lamp: MSD 250/2 Philips, CSD 250/2/SE GE, HSD 250/78 Osram
Average service life: 2000h Philips, 2000h GE, 3000h Osram
Color temperature: 8500k Philips, 8500k GE, 7800k Osram
Luminous flux: 18.000lm Philips, 18.000lm GE, 17.000 Osram
Weight and dimension
Dimension: 375 x 430 x 450 mm
Weight: 21,5 kg
Electromechanical effects
Pan: 540° 16bit (position feedback)
Tilt: 280° 16bit (position feedback)
Gobowheel: 6 rotating and positionable gobos + open 2 glass gobos, 4 metal gobos, all gobos interchangable
Colorwheel: 11 dichroic colorfilter + white, 12 bicolors slow rotation to fast rainboweffekt
Focus: 2 m - infinity (motorized)
Prism: rotating and positionable 3-facet prism slow to very fast rotation
Dimmer: mechanical dimmer 0-100%
Shutter: mechanical high-speed shutter 0-10Hz
Other effects
Laser: 4,5 mW laserdiode with DMX control
Optical system
Projection angle: 15° (optional 18°)
High quality, coated condensor optics: high light output with an even lightbeam
Gobos
Outside diameter: 27 mm
Image diameter: max. 23 mm
Thickness stainless steel gobo:0,15 mm
Thickness glass gobo: 1,1 mm
Control
Protocol: USITT DMX 512
DMX-Channels: 15
Musiccontrol: internal microphone, master-slave function, gobo-, colorchange and shutter control with music
Lamp on/off: by DMX or automatic
User board
Easy DMX address setting
Operation hour meter
Lamp hour meter
Temperaturecontrol
Testmode
Audiomode
Manual control of all functions
DMX-Input value readout
Programming
Internal movements
Separate speed for Pan/Tilt
Random strobe
pulse effect
colorchaser
goboshake
Master-Slave function
Audiomode with different zeroposition and different sizes
When the DMX-signal is lost the audiomode will be switched on automatically if required (especially for clubs)
Installation
4 x M 10 inserted nut to mount a clamp or half-coupler
2 x mounting plates for wall mounting
Any orientation
Power consumption
230 V/50 Hz 400 W
Included items
2 x mountingplate for wall mounting
3 x spare gobos
1 x document box
1 x spare parts box