Moving Magnet Phono Stage
Compact MM phono stage in high quality metal enclosure.

The new MM 002 phono preamplifier replaces the renowned MM 001. Developed from the ground up, the MM 002 is a clear step forward, offering excellent Moving Magnet sound quality, and exceptionally low noise levels, at a very affordable price point.
Specification
- Mode Moving Magnet (MM)
- Gain at 1 kHz: 40 dB
- Cartridge matching (input impedance): 47 kOhms + 220 pF fixed
- Frequency response: 10 Hz - 50 kHz (-3 dB)
- RIAA curve accuracy: 0.3 dB max.
- THD+N: <0.015%
- Signal-to-noise-ratio: >86 dB
- Crosstalk: ≧40 dB
- Input sensitivity: 3.14 mVrms for -10 dBV output (316 mVrms)
- Max. output voltage: 498 mVrms at 5 mVrms input (1 kHz)
- Output impedance: 47 Ohms
- Input connections: 1 pair of RCA sockets (left/right)
- Output connections: 1 pair of RCA sockets (left/right)
- Power supply: 24 V DC / 630 mA
- Power consumption: 3.3 W / 15 mA
- Weight: 292 g (not including power supply)
- Dimensions (W x H x D): 100 x 45 x 93 mm