Specifications
- Mode: MM/MC (switchable)
- Gain at 1 kHz: 40 dB (MM)/60 dB (MC)
- Input impedance (MM): 47 kΩ + 220 pF fixed
- Input impedance (MC): 47 kΩ + 1 nF (modifiable with external load plugs)
- Frequency response (flat): 20 Hz - 20 kHz ±0.3 dB
- Frequency response (-3 dB): 10 Hz - 50 kHz
- RIAA curve accuracy: ±0.3 dB
- THD+N: <0.013% (MM)/<0.055% (MC)
- Signal-to-noise ratio: >86 dB (MM)/>72 dB (MC)
- Crosstalk: ≧40 dB
- Input sensitivity (MM): 3.29 mVrms for -10 dBV output (316 mVrms)
- Input sensitivity (MC): 0.325 mVrms for -10 dBV output (316 mVrms)
- Max. output voltage: 482 mVrms at 5 mVrms input (1 kHz)
- Output impedance: 47 Ω
- Input connections: 3 pairs of RCA sockets (left/right)
- Output connections: 1 pair of RCA sockets (left/right)
- Power supply: 24 V DC
- Power consumption: 3.4 W/15 mA
- Weight: 504 g (not including power supply)
- Dimensions (W x H x D): 150 x 50 x 117 mm