BRONZE SERIES 6 BLACK OAK
From the towering Bronze 6, the most complete new Bronze speaker, music and home theatre lovers can appreciate the full-range flavour of our forty year design heritage.

Its deceptively compact cabinet supports two 6 1/2” C-CAM bass drivers operating in tandem with a further 6 1/2” mid-range unit housed in a dedicated chamber.
In this way matching drivers tuned for different roles are able to develop a wonderfully uniform, tonally consistent sound-field involving seismic low bass and richly coherent mid-range detail, which rises in frequency to meet the illuminating resolution of our fabulous Bronze C-CAM tweeter.
Here is new Bronze in tooth and claw, alive to its ambitious audiophile design precedents and equipped with a compelling mix of accuracy, scale and dynamics for the highest value music and home theatre audio.
Features
- New C-CAM® gold dome tweeter
- Optimised 6 1/2” mid-range driver featuring concave ‘dished’ C-CAM® cone profile
- Dual 6 1/2” bass drivers featuring concave ‘dished’ C-CAM® cone profile
- Two and a half way configuration with differentially tuned acoustic system - higher efficiency and improved low frequency extension
- HiVe® port technology
- All drivers feature single bolt-through driver systems, for increased overall bracing, rigidity and driver/baffle de-coupling
- High quality crossovers with premium grade Polypropylene film capacitors used throughout
- Rigid 18mm MDF construction throughout, employing radial and cross-bracing techniques for high rigidity resulting in low cabinet coloration
- Floor-level terminal panel for easy termination and neat cable access. Bi-wire/ Bi-amp terminal configuration
- Premium quality vinyl veneer finishes
Specification
- System Format: 2 1/2 Way
- Frequency Response: 34Hz - 30kHz
- Sensitivity (1W@1M): 90dB
- Nominal Impedance: 8Ω
- Maximum SPL: 114.8dBA (pair)
- Power Handling (RMS): 150W
- Recommended Amplifier Requirements: 40-150W
- Cabinet Design:
  - Bass section - Front/rear bass reflex with HiVe®II Port technology.
  - Sealed mid-range enclosure.
- Crossover Frequency:
  - LF: -6dB @ 150Hz
  - MF/HF: 2.5kHz
- Drive Unit Complement
  - 2 x 6 1/2" C-CAM® bass
  - 1 x 6 1/2" C-CAM® bass mid-range driver
  - 1 x 25 mm gold dome C-CAM® tweeter
- Cabinet Dimensions (H x W x D): 985 x 185 x 315 mm
- Dimensions (Including Grille, Terminals, Plinths & Spikes (H x W x D)): 1033 x 235 x 350 mm
- Weight (each): 16.6kg (36lbs 8oz)