All the wonder of Platinum II’s crystal clear tonal precision is concentrated by this beautiful little two-way speaker comprising a single 6.5” RDT®II mid-bass driver and MPD tweeter. Easy to place in-room the PL100 II will nevertheless belie its compact dimensions with a wide open soundstage punctuated by breath-taking dynamics and imaging so stable you can almost touch it. A bespoke floor stand (available separately) will position the PL100 II at the perfect listening height.

Features
- 6 1/2" RDT®II bass / mid driver
- MPD (Micro Pleated Diaphragm) high frequency transducer designed specifically for Platinum II
- Single rear HiVe®II port
- New patented 'DCF' (Dynamic Coupling Filter) mechanism for more natural sound
- Bespoke speaker terminals and footings
- Underhung, edge-wound voice coils: greater driver efficiency and lifelike dynamics, less distortion
- Bolt through drivers: clearer sound and cleaner aesthetics
- Anti-Resonance Composite (ARC) mid-range housings and baffle components: reduced cabinet vibration, purer sound quality
- Hand-upholstered front baffle: the very highest quality Inglestone leather supplied by Andrew Muirhead
- Individual driver grilles
- Finish options: Santos Rosewood or Ebony natural wood veneers with clear gloss piano lacquer, or Piano black gloss lacquer
- Optional dedicated floor stand available
Specification
- System Format: 2 Way - 2 Driver
- Frequency Response (-6dB - IEC 268-13): 40Hz - 100kHz
- Sensitivity (1W@1M): 88dB
- Maximum S.P.L.: 111.8dBA (pair)
- Nominal Impedance: 6Ω (4.5Ω min. @ 160Hz)
- Power Handling (RMS): 120W
- Recommended Amplifier Requirements (RMS): 60 - 120W
- Cabinet Design: Single rear HiVe®II port
- Drive Unit Compliment:
- 1 x 61/2" RDT®II bass / mid driver
- 1 x MPD high frequency transducer
- Crossover Frequency: 3.0kHz
- External Dimensions (H x W x D):
- 370 x 225 x 285mm
- (149/16 x 87/8 x 111/4”)
- Weight (each): 14.94kg (32lb 14oz)