FLOORSTANDING LOUDSPEAKER
Building on the success of the award-winning S30 bookshelf speaker is the S70 floorstanding loudspeaker which combines excellent treble and commanding bass performance for an outstanding sound.

With a soft dome tweeter for detailed and realistic treble, the S70 also features two impressive mid/bass drivers for powerful low frequencies.
The elegant and slimline cabinet is carefully braced for maximum rigidity while spiked plinths offer superb stability. The S70 has three-way gold plated biwirable terminals and is magnetically shielded for ease of placement.
Features
- Compact, sleek design
- Bi-wirable
- Magnetically shielded
- Available in dark oak and noir
- Easily removable grilles
- Spiked plinth for ultimate stability
Specifications
Sensitivity:	90dB
Frequency Response:	39Hz - 20kHz
Nominal Impedance:	4-8 Ohms
Drive units:	Tweeter: 1 x 25mm (1”) Woofer: 2 x 130mm (5") mid/bass driver
Crossover:	2nd Order 2.5 way
Recommended maximum amplifier power:	120 Watts
Magnetically shielded:	Yes
Dimensions (W x H x D):	160 x 938 x 240mm (inc. grill) (6.3 x 36.9 x 9.4”)
Weight:	12.4Kg (27.3lbs)
Finishes:	Dark Oak Noir