CLASS D POWERED SUBWOOFER
The Radius 390 comprises of colour-coded 10” C-CAM® active/ABR drivers, powered by a 220W Class D amplifier. Enjoy rapid EQ optimisation from Impact, Music and Movie settings, and system automation via the 12V trigger.

Features
- 18mm MDF cabinet construction with internal bracing
- Cool-running 220W Class D amplifier with switch mode power supply (SMPSU)
- Twin side-firing 10” C-CAM® drivers - one active and one passive ABR
- Low pass filter switch – for LFE or Stereo input selection
- Power switch with ON – Auto- Off/ trigger settings
- Stereo/ LFE RCA inputs
- 3 x Pre-set EQ settings – Music/Movie/Impact
Specification
- System Format: Active sub-woofer system – Auxiliary (ABR) loading. 18mm MDF cabinet
- Low Frequency Limit: 30Hz (- 6dB)
- Upper Frequency Limit: Variable 40 – 120 Hz @ 24dB/Octave
- Amplifier Power Output: 220 Watts @ 1% THD+N
- Amplifier Classification: Class D amplifier with Switch mode power supply (SMPSU)
- Bass EQ Switch: Music / Movie / Impact
- Phase Control: 0 & 180 degrees
- Auto Sensing: Line Level >3.5mV
- Input Level Requirements: Standby after approximately 15 minutes if no signal sensed
- Driver Compliment:
  - 1 x 10” (250mm) C-CAM® long throw driver
  - 1 x 10” (250mm) Auxiliary bass radiator
- Input Impedance: > 20K Ohms
- Mains Input Voltage: AC 110 - 120 V ~ 50/60Hz;  AC 220 - 240 V ~ 50/60Hz  (Factory Region Preset)
- Dimensions including amp & feet (HxWxD): 348 x 330 x 345mm (1311/16 x 13 x 129/16 Inches)
- Connections: Stereo RCA in, LFE in, 12v Trigger in  (3.5mm mono mini-jack)
- 12v Trigger Input: 5 - 12v via 3.5mm mono mini-jack socket
- Power Consumption: 220 Watts / 0.5 Watts in Standby (ErP approved)
- Weight (Unpacked): 13.76Kg (30lb 4oz)